## Slide 1: LiDAR 01: Introduction
Networked Systems Lab @ Chung-Ang University
Kyungmin Kim
Chung-Ang University
kyungddin@cau.ac.kr
Jul. 17th 2025

## Slide 2: Overview
In this lecture, you will learn..
  What is LiDAR?
  How to connect Ouster LiDAR?
  Various LiDAR Frameworks Introduction
  LiDAR Visualization
  Open3D: Nice and Easy Framework

## Slide 3: Notice!
Recommend to work in Linux environment
  Many LiDAR Frameworks work well in Linux environment.
For version management
  Anaconda is recommended.
  You will experience many package problems..
Some steps may change in the future
  You need to check official document.

## Slide 4: LiDAR Sensor Introduction
What is LiDAR?

## Slide 5: LiDAR Introduction
Light Detection And Ranging
  a.k.a LiDAR
  Sensor that uses laser reflection.
  Through this, It can measure distance & shape.
LiDAR collects various physical quantity
  Distance, Reflectivity, Angle, Return Number…

## Slide 6: LiDAR Introduction: Ouster OS1-32
Ouster LiDAR Sensor
  Powerful and Expensive LiDAR Sensor.
  Lecture Standard: Ouster OS1-32
Ouster OS1-32 Spec
  Maximum Distance: 120M
  Vertical Angle: 22.5o
  Horizontal Angle: 360o
22.5o
120m

## Slide 7: LiDAR Connection Step
Now let’s connect Ouster LiDAR!

## Slide 8: LiDAR Connection Step
To use Ouster LiDAR
  Step1: Hardware Connection
  Step2: Network Setting
Step1:
Hardware Connection
Step2:
Network Setting

## Slide 9: Hardware Connection
Step 1

## Slide 10: Hardware Connection
Hardware Essential Component
  PC
  Interface Box
    Transmit data between PC and Sensor
  Ethernet Cable
    Cable between PC and Interface
  Ouster LiDAR
  Power Supply/Battery

## Slide 11: Hardware Connection
Ethernet
Cable
Ouster LiDAR
Interface
BOX
Power
Supply

## Slide 12: Hardware Connection
Ethernet
Cable
Power Cable
LiDAR Connection Step 1
  Connect Ethenet cable & Power cable to Interface Box.

## Slide 13: Hardware Connection
LiDAR Connection Step 2
  Connect Power cable to Power Supply(Battery).
    A green light turns on when the power is on

## Slide 14: Hardware Connection
Connect to USB Port!
LiDAR Connection Step 3
  Connect Ethernet cable to PC.

## Slide 15: Hardware Connection
LiDAR Connection Step 4
  Connect Interface Box to Ouster LiDAR.
    Align Red line to “UP” text.
    Turn clockwise until you hear a “Click!” sound.
Red Line!

## Slide 16: Hardware Connection
OS1-32 Cautions
  Don’t touch the Window!
    There’s Laser out and Receiver.
  Watch out for LiDAR Overheating!
    Recommended usage time is 4 hours.
Need to cool down
After 4 hours! 

## Slide 17: Ubuntu Network Setting
Step 2

## Slide 18: Ubuntu Network Setting: PC Network
LiDAR Communication
  LiDAR uses UDP Protocol
    Set Ethernet static IP address
    Assign DHCP IP address to LiDAR sensor
PC
Static IP
Sensor
DHCP IP
UDP Network 192.168.0.XX
Why use the DHCP protocol?
1. To simplify configuration for multiple LiDAR connections
2. To prevent IP address conflicts

## Slide 19: Ubuntu Network Setting: PC Network
PC Network Setting
  Linux Setting: “Network Setting – USB Ethernet – IPv4”
    Select Static and enter IP Address and Netmask.
  Address: 192.168.0.XX (XX is your choice; 0 ~ 100) Netmask: 255.255.255.0

## Slide 20: Ubuntu Network Setting: PC Network
PC Network Setting
  $ ifconfig to check network setting.
    Check network setting and Device name! (for Sensor Network)

## Slide 21: Ubuntu Network Setting: Sensor Network
Sensor Network Setting
  $ sudo dnsmasq –C /dev/null –kd –F 192.168.0.0,192.168.0.100 –i <device_name> –bind-dynamic
    <device name> is your device name.
  Check Terminal whether DHCP IP is addressed.

## Slide 22: Ubuntu Network Setting: Shell Script
Shell Script Guide
  It’s annoying to do this every time. We use Shell Script!
  Make dhcp.sh file to your home directory.
  Open your text editor(e.g. vim, nano) and write #!/bin/bash sudo dnsmasq –C/dev/null –kd –F 192.168.0.0,192.168.0.100 –i [device_name] –bind-dynamic

## Slide 23: Ubuntu Network Setting: Shell Script
Shell Script Guide
  $ sudo chmod _x ~/dhcp.sh to add execution permission.
  $ ./dhcp.sh to get DHCP IP quickly!
Step1:
Hardware Connection
Step2:
Network Setting
Complete!!

## Slide 24: Ubuntu Network Setting: Sensor Network
Process is still alive!
DHCP Re-Address
  When you close the terminal, power off the sensor or whatever. there’s still DHCP address in the process..
  You must kill the process by $ sudo pkill -9 dnsmasq

## Slide 25: Ubuntu Network Setting: Browser Network Setting
Internet Browser Network Setting
  After connection, you can use browser network setting.
  Open your internet browser and enter your sensor address.
  You can check sensor information and configure sensor setting!

## Slide 26: LiDAR Frameworks
To help you control LiDAR

## Slide 27: LiDAR Frameworks
LiDAR Frameworks
  There are many LiDAR Frameworks to help you control the LiDAR.
    Hardware Company’s SDK(Software Development Kit)
    ROS
    Programming Library
  To send sensor data to your program, Ouster SDK is a good choice.
SDK | ROS | Library

## Slide 28: LiDAR Frameworks
LiDAR Frameworks Example
  Ouster SDK
    Official SDK for Ouster LiDAR
  ROS
    Middleware for Robotics and LiDAR Sensor
  Open3D
    Python/C++ Point Cloud Library
  PCL
    C++ Point Cloud Library

## Slide 29: Point Cloud Visualization
Visualize Sensor’s Data

## Slide 30: Point Cloud Visualization
Point Cloud
  Converted LiDAR data
  Each Point has (X,Y,Z) spatial information.
Point Cloud Visualization
  Connection is complete. But we don’t know what exactly happened inside.
  We need to visualize Point cloud to see what is going on!
01000101 010010^^
1011101 011011?
OMG!!

## Slide 31: Point Cloud Visualization
Visualization!
Point Cloud Visualization Tool Examples
  Ouster Studio
    Official Ouster Visualization Program
    Easiest way to visualize Point Cloud!
  Rviz
    ROS Visualization
  PCL
    C++ Point Cloud Library
  Open3D
    Python Point Cloud Library

## Slide 32: Point Cloud Visualization
Visualization!
Point Cloud Visualization Tool Examples
  Ouster Studio
    Official Ouster Visualization Program
    Easiest way to visualize Point Cloud! (We use this program!)
  Rviz
    ROS Visualization
  PCL
    C++ Point Cloud Library
  Open3D
    Python Point Cloud Library

## Slide 33: Point Cloud Visualization: Ouster Studio
How to use Ouster Studio?
  Go to Ouster Studio web page and download Linux(IMG) file.
    https://ouster.com/ko/products/software/ouster-studio

## Slide 34: Point Cloud Visualization: Ouster Studio
How to use Ouster Studio?
  “Properties – Permissions – Check Allow executing file as program”
  Run the Image file.

## Slide 35: Point Cloud Visualization: Ouster Studio
How to use Ouster Studio?
  Select your sensor and click “configure and Visualize”.

## Slide 36: Point Cloud Visualization: Ouster Studio
Now you can see Point Cloud!

## Slide 37: Ouster SDK & Open3D Introduction
Utilize Point Cloud Data

## Slide 38: Ouster SDK
OUSTER SDK
Get Sensor Data
Open3D or PCL
Process Point Cloud Visualization
Ouster SDK
  SDK that reads, parses and visualizes the sensor data
  Usually use to read sensor data
    Recommend to use other libraries to process the point cloud

## Slide 39: Open3D Library
Python/C++ library to process 3D data like Point Cloud
  Recommend Python language.
Key Features
  Visualization
  Voxel Downsampling
  Point Cloud Painting
  Point Cloud distance calculation
  Bounding Volume
  Segmentation Plane
  Etc..

## Slide 40: Ouster SDK & Open3D
Library Installation
  Open Linux terminal and command $ pip install ouster-sdk $ pip install open3d
To check installation and version
  Command $ pip show ouster-sdk $ open3d –version

## Slide 41: Ouster SDK & Open3D: Example
1. Module Import
>> ouster.sdk and open3D
2. Ouster.sdk >> Get Sensor Data
3. Open3D >> Process Point Cloud
Code Example 1

## Slide 42: Ouster SDK & Open3D: Example
Visualization Example 1

## Slide 43: Ouster SDK & Open3D: Example
Code Example 2
1. Get sensor data by using ouster.sdk
2. Process by using open3D (Voxel downsampling, Noise Filtering, distance Limitation, etc)

## Slide 44: Ouster SDK & Open3D: Example
Visualization Example 2

## Slide 45: Reference
Ouster SDK
  https://static.ouster.dev/sensor-docs/image_route1/image_route2/connecting/connecting-to-sensors.html
  센서값을 받기 위한 공식 SDK
Ouster Studio
  https://ouster.com/products/software/ouster-studio
  빠른 시각화 소프트웨어
PCL: Point Cloud Library
  https://pointclouds.org/
  포인트 클라우드 제어를 위한 C++ 라이브러리
PointPillars
  https://github.com/zhulf0804/PointPillars
  객체 인식을 위한 라이브러리
Open3D
  https://www.open3d.org/docs/release/
  포인트 클라우드 제어를 위한 Python 라이브러리

## Slide 46: Thank you!
Questions?